## Slide 1: blinky
Adam Barney
Quicken Loans
Senior Software Engineer
adambarney@quickenloans.com
beyond
making a “REAL” IoT thing
Notes: up with

## Slide 2
Quicken Loans
TECHNOLOGY

## Slide 3
blinky
Notes: This is the “Hello World!” of the Maker world – pretty much the first thing you do when getting started.

## Slide 4: now
what?
Notes: But now what? You have an extraordinary amount of computing power in your hand with limitless possibilities, so what can you do?
I’ll ask the audience for ideas that they’ve had, or projects they’ve made

## Slide 5
Notes: So what did I decide to make? Well, this is our sauna that we have at our family vacation spot in northern MN. The basic idea of a sauna is that you get very hot and sweaty – to the point where virtually every pore is open and sweating profusely, then you run out and jump in a relatively cool lake, which slams all those cleared out pores shut almost instantly. They are called “Finnish Baths” as well, and the true Finns will cool themselves off by doing pullups through a hole in the ice!

## Slide 6
Notes: Inside is a wood burning stove with rocks on top of it. We heat the room up to about 150-185 degrees Fahrenheit, then throw water on the rocks to fill the room with steam.
It takes an hour or two to get it up to temperature when starting it cold. Most of that time is spent waiting. Or walking down to check the temperature.

## Slide 7
Notes: It’s not a LONG walk, but it’s not super short, either. There’s our cabin on the right, and the sauna on the left.
What I wanted to do is create a way to check on the current conditions of the sauna without having to walk down there myself to check on the temperature.
And anything worth doing is worth overdoing, right? Others on our beach use it, so I also wanted to know whether our neighbors were currently using it at the time or not.
And I love science. And data. So I wanted to log temperature, humidity and whether there were people in it, when the door opens and closes so I can get an idea about what pouring water on the rocks really does to the temperature and humidity. We always berate people for opening the door, but what effect does opening the door really have on the interior conditions? I aimed to find out.

## Slide 8: the
problem?

## Slide 9
i’m lazy

## Slide 10: the
solution?

## Slide 11
technology

## Slide 12
challenges
the
Notes: As with any project, there will be problems that need to be solved. In the maker world, the problems are far different than those you might expect to see in a software solution. It’s part of what makes creating something to live in and interact with the real world difficult, challenging and rewarding.
No power at the sauna
No internet at the sauna
The sauna is over 200 feet away
With a forest in between
The sauna gets HOT - up to 100 degrees Celsius
Heat and humidity varies around the room
The sauna's charming, and should stay that way
This is not my full-time job

## Slide 13: the basic
solution
Notes: I found parts that would do what I needed. A temperature and humidity sensor, a motion sensor, a door sensor, and an LED readout for the temperature. All of these were connected to an Arduino uno to begin with.

## Slide 14
Notes: This was the first prototype of the Sauna Monitor

## Slide 15: challenge #1:
distance
Notes: The first problem to tackle was how do I display information from the sensors in the sauna somewhere in the cabin, which is a minimum of 200 feet away?
It’s too far to run jumper wires all that way (the signal would degrade over those distances)
I thought about trying to get the sauna pieces connected to the internet, but it’s far too far away from any wifi sources

## Slide 16
“server” unit – v1
Notes: So the solution was to split it in to two parts – a Client unit, which would be in the sauna, and a Server unit which would stay in the cabin.
The Server unit was created with an Adafruit Huzzah breakout, which has built-in wifi, an LCD display, and an nRF2401L radio receiver to communicate wirelessly with the sauna unit.

## Slide 17: challenge #2:
power
Notes: Now that we can communicate between the sauna and the cabin, we can turn our attention to power.
There is no power anywhere near the sauna, so it will need to be battery powered, but I do not want to constantly be changing the batteries.

## Slide 18
Notes: My first approach was to use a LiPo battery and solar cell. My hope was to limit the power use of the client unit so that it could be powered by the solar cell, with the battery as a backup.
Unfortunately, in order to get the solar cell anywhere where it would generate usable current, I would need to run wires 20-30 feet away from the sauna. This is still an option later, but for v1, I didn’t want to add that as a complexity.
So I turned my attention to reducing the power consumption as much as possible

## Slide 19
Arduino Uno ATMega328
Notes: The Arduino Uno, along with other prototype boards are very convenient and easy to use when experimenting and developing a proof of concept. But the things that make them easy to use also makes them inefficient. They’re not designed to be used “in production” – they simply provide common extras you might need when first starting work with a microcontroller chip.
In this case, the microcontroller is the ATMega328. We can save a TON of power consumption by switching from the full Uno to just the chip. If we were to go with the SMD version of the chip, power consumption is even less.
And look at the prices as well – no consumer product would contain a $22 Arduino in a finished product.

## Slide 20
Notes: In order to see if I was making progress with power savings, I built this device to measure the current draw from my circuit.

## Slide 21
using the
ATMega328
by itself
Notes: The AYMega328 can be used without the Arduino Uno in this way. If you examine the Uno itself, you’ll see the ocmponents in this schematic on the board, plus a bunch of things we don’t NEED.

## Slide 22
run the processor at a lower frequency
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 23
run the processor at a lower frequency
run the processor at a lower voltage
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 24
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 25
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 26
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 27
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 28
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
put the processor to sleep
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 29
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
put the processor to sleep
don't use inefficient voltage regulators
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 30
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
put the processor to sleep
don't use inefficient voltage regulators
don't use power-hungry displays
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 31
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
put the processor to sleep
don't use inefficient voltage regulators
don't use power-hungry displays
wake the processor from sleep only when needed
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 32
run the processor at a lower frequency
run the processor at a lower voltage
turn off unneeded internal modules in software
turn off brownout detection
turn off the Analog-to-Digital converter (ADC)
turn off the watchdog timer
put the processor to sleep
don't use inefficient voltage regulators
don't use power-hungry displays
wake the processor from sleep only when needed
turn off external devices until needed
optimizing power
Notes: There’s a great site (link lower right) that details several things that can be done to reduce the ATMega’s power consumption from tens of milli-amps to as low as a couple micro-amps.
I used some of these, but not all. (briefly describe which were used, which weren’t and why)

## Slide 33
Notes: This is the client module when it was running off of the Uno itself. Notice the current draw – 105 mA. On a 2500mAH batter, that gives us about a day of use

## Slide 34
Notes: Now notice that I have the ATMega chip on the breadboard, without the Uno. Power use here is 13mA, or about 8 days worth of usage. I eventually got it down to about 8-9 mA, or almost 2 weeks. My plan was to purchase a 20,000 mAH battery, which would give me 4 months – the whole summer!
can produc
For reference, the solar cell in full sunlight can generate up to 330mA – more than enough to power the unit and keep a battery fully charged for use at night and during overcast days.

## Slide 35: challenge #3:
heat
Notes: It was about this time that I started thinking about how the components might stand up to the unique environment – very hot and very humid. A good sauna is about 150-185 degrees F (65 – 85 degrees C), but they can get up to 210, or almost 100 C. How would things stand up? To find out, we need to check all of the components datasheets!

## Slide 36
    1.8 – 5.5 v
Temperature Range:
    -40oC to 85oC
Speed Grade:
Notes: This is the ATMega328 data sheet. That operating range is borderline for our sauna range. Chances are it would be ok, but we’d be pushing it.

## Slide 37
Component | Maximum Operating Temperature
ATMega328 | 85℃
Battery | 60℃ (with lower performance) and RISKY!
Ceramic Capacitors | 85℃
Oscillator | 70℃
nRF24L01 | 85℃
LED Display | 85℃
PIR Motion Display | 50-60℃
DHT22 | 125℃
check your data sheets!
Notes: Other components have issues too. The Oscillator will start fluctuating if the temperature changes too much, and it has a narrower range. Some of our less critical sensors are on the edge too, but slightly skewed readings wouldn’t be awful. The LiPo battery is the biggest concern. Even at 60 C, the life and output of the battery is significantly effected, and those things have a history of doing bad things (like exploding or catching fire) when they are stressed.
The important parts of the client unit can’t be in the sauna itself. So, what to do?

## Slide 38
client base unit
sensor unit
Notes: I split it up in to two units

## Slide 39
PCB design
making it real:
Notes: A breadboard with wires and components hanging all over the place is not something you’d ever go to market with. To make a “real” product, you need to make Printed Circuit Boards (PCBs)

## Slide 40
PCB Layers
(2-layer PCB)
top silkscreen
top solder mask
top copper
PCB board
bottom copper
bottom solder mask
bottom silkscreen

## Slide 41
PCB designer choices
+ many, many, more

## Slide 42
demo:
easyEDA

## Slide 43
make your own
have it manufactured

## Slide 44
lessons learned
check your schematic

## Slide 45
lessons learned
check your schematic
check you schematic again

## Slide 46
lessons learned
check your schematic
check you schematic again
check your part numbers

## Slide 47
lessons learned
check your schematic
check you schematic again
check your part numbers
check those again too

## Slide 48
lessons learned
check your schematic
check you schematic again
check your part numbers
check those again too
through-hole components are easier, but SMD is how things are done

## Slide 49: making it real: enclosures

## Slide 50
3-D design software

## Slide 51
demo:
fusion 360

## Slide 52
lessons learned
measure twice, model once

## Slide 53
lessons learned
measure twice, model once
plan a couple iterations of design & printing

## Slide 54
lessons learned
measure twice, model once
plan a couple iterations of design & printing
0.25-0.5 mm tolerances for press-fit interfaces

## Slide 55
lessons learned
measure twice, model once
plan a couple iterations of design & printing
0.25-0.5 mm tolerances for press-fit interfaces
fusion 360 is a powerful tool

## Slide 56
lessons learned
measure twice, model once
plan a couple iterations of design & printing
0.25-0.5 mm tolerances for press-fit interfaces
fusion 360 is a powerful tool
make sure printing material works for your environment

## Slide 57
let’s talk about IoT

## Slide 58
putting it
all together

## Slide 62: up to the lake!

## Slide 63: it didn't work

## Slide 64: the problem:
distance & trees
Notes: I found parts that would do what I needed. A temperature and humidity sensor, a motion sensor, a door sensor, and an LED readout for the temperature. All of these were connected to an Arduino uno to begin with.

## Slide 65: other challenges
wiring from client unit to sensor unit
placement of sensor unit
still rather invasive and obvious
couldn't post to Azure table storage
enclosures all need another iteration or two

## Slide 67: the makers
toolbox

## Slide 68
future projects
“parking partner” v2
video spotter for boat
sous vide cooker
r/c submarine
sprinkler controller

## Slide 69
Adam Barney
Quicken Loans
Senior Software Engineer
adambarney@quickenloans.com
Thank you!
Notes: up with